Antennas in plasma: Numerical calculation
Presentation of the PhD Thesis by Thomas Oswald
At Karl-Franzens-Universität Graz, supervised by Prof. H.O. Rucker

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Modeling the plasma sheath
- Conclusion + Outlook

---
Introduction: Radio Experiments
- Radio experiments are one of the most important experiments on spacecraft
- By receiving and analyzing radio and plasma waves created by natural phenomena, the physics of the creation process can be studied.
- Radio and plasma waves are received by antennas which are the interface between free wave propagation and guided wave propagation
- My thesis deals with the radio frequency range (kHz-MHz)

---
Introduction: Antennas
- Scientific antennas are monopoles which are either driven against another monopole to for a dipole, or against the spacecraft body.
- For the correct interpretation of the received data, the antenna properties must be known accurately
- Those are influenced by the spacecraft body and the surrounding plasma
- The influence is highest near the plasma resonance frequencies but also noticeable at the higher parts of the typical radio experiment frequency range.

---
Introduction: Properties
- The most important properties are:
  - Power patterns
  - Impedances
  - Admittances
  - Effective length vectors
- Usually a vacuum is postulated

---
Introduction: Calibration methods
- Numerical calculation
- Rheometry
- Anechoic chamber
- Inflight calibration

---
Introduction: Numerical methods
- Method of Moments(MoM)
- Finite difference, time domain (FDTD)
- Finite element (FEM)
www.thecomputationalphysicist.com

---
Introduction: MoM
- The MoM is a boundary value method
- The spacecraft is modeled as a grid of wires or patches
- Then the currents as a response of a 1V excitation along these wires/patches are computed
- This calculation is performed with an appropriate solver
- On basis of the current distribution, all other antenna properties (effective length vectors, impedances) can be calculated with MATLAB routines

---
Introduction: Putting plasma into the MoM
- The effect of surrounding plasma is small but measurable at radio frequencies.
- Two Methods:
  1. The dielectric plasma mode: plasma physics in is the equivalent dielectric tensor.
  2. Modeling the plasma sheath: The plasma effect manifests itself in a capacity and resistivity which can be included easily in the calculation.

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Modeling the plasma sheath
- Conclusion + Outlook

---
Method of Moments
- MoM is a method to solve field problems which can be described with the theory of linear spaces.
- L(j)=g
  - L...operator, functional
  - j...response function to be determined
  - g...excitation
- In the MoM this equation is converted to matrix form and solved numerically
- To solve electromagnetic scattering problems:
  - g...excitation voltage
  - j...the surface current system
- L must have certain properties which are governed by the theory of linear operators (e.g. self-adjointness,...)

---
Method of Moments
- A suitable inner product has to be defined
- The inner product has to have certain properties:
- A suitable inner product for our purpose is
- The function to be determined has to be expanded:
- Jn forms a set of independent basis functions
- Cn are coefficients to be determined
- Substituting for j in the linear equation gives
langle f , g rangle
langle f,g rangle = langle g,f rangle newline langle af+bg,h rangle = a langle f,h rangle + b langle g,h rangle newline langle f^{*},f rangle > 0 if f <> 0 newline langle f^{*},f rangle = 0 if f = 0
langle f,g rangle = int f(x)g(x) dx

---
Method of Moments
- The inner product with a weighting or testing function is formed:
- This can be written as matrix equation:
  The solution can be found my standard methods of linear algebra.
- Then the currents can be reconstructed.
- For electromagnetic theory the equation can be written as
- When the antenna is excitec by a unit voltage, V or g is a vector with zeros and a single entry which is 1 at the feed.
- When the excitation is by an incoming wave, the vector is

---
MoM: Basis and Testing functions
- In infinite set of combinations of basis and testing functions lead to success
- They differ in accuracy and convergence.
- For basis functions, constant functions (MEC), linear function (Concept II) and sinusoidal functions (ASAP, NEC, MEC) are common.
- For patches, spacial functions have to be used.

---
MoM: Basis and Testing functions
- For testing functions it is common to use the same functions as basis functions (Galerkin method).
- An other method is to use Dirac delta functions (collocation method).
- The collocation method facilitates the integration to get the matrix elements.
- This way the function is forced to fit at a single point.

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Conclusion + Outlook

---
Theory: Electrodynamics
- Starting point: Maxwell
- And Constitutive equations
- A similar equation would exist for the magnetic field but is not necessary, because all the physics can be included in the equivalent dielectric tensor.
- If the material is linear and space and time are homogeneous, the equations can be Fourier transformed. When external sources are not present:
- and
- where

---
Theory: Electrodynamics
- Often potential fields are used to facilitate finding solutions:
- They are not unique, so gauge conditions are used:
- Lorenz gauge, Coloumb gauge, temporal (Weyl) gauge
- In plasma it is often better to use the fields directly, since there is no gain in solving for A instead of E.
- Maxwell's equation can be manipulated to form a wave equation:
- Or: using the
  diffraction index
- Since

---
Theory: Electrodynamics

---
Theory: The equivalent dielectric tensor
- Includes all plasma physics in the dielectric model.
- Describes the linear response of a medium to electromagnetic disturbances.
- Is a tensor in general.
- Can be complex. The imaginary part can be interpreted as a damping effect.
Ohm's law

---
Theory: Cold isotropic plasma
- The cold isotropic dielectric function is a scalar function of the frequency.
- It is real valued.
- Can easily be derived by using the Polarization:
- And solving Newton's equation.
  For r. One gets:
- Using
- One gets
- Hence
- The isotropic dielectric tensor can be inserted to all MoM solvers, so this result can be used immediately

---
Theory: Cold magnetized plasma
- The dielectric tensor of magnetized cold plasma is well known.
- It can be derived by using Newton's equation with the magnetic field.
- The subscript is to show that it is an external static field.
- The result:
- Or when factorizing for lh and rh polarization:

---
Theory: Kinetic isotropic plasma...electrostatic approximation 1
- Kinetic theory finds many wave-modes.
- Above characteristic frequencies and without magnetic field, 2 types are important:
  - Langmuir waves
  - EM waves
- Basis: Vlasov equation
- And perturbation theory.
- E-field || k
- After Fourier transform one gets:
  one can use scalar potential and Poisson eq. as second function:
- Results in:

---
Theory: Kinetic isotropic plasma...electrostatic approximation 2
- Can be identified as dispersion relation. Hence:
- The integral can not be evaluated since it contains a pole.
- Landau found a solution by making the frequency complex:
- Integrated along a contour around.
- This leads to the famous collision-less Landau-Damping.
- ...which means the Langmuir waves are so heavily damped that we will never receive such waves from a distant source in the RF-range.
- But these waves are important for quasi-static thermal noise analysis.

---
Theory: Kinetic isotropic plasma...EM waves
- Using the same procedure but retaining the vector form, one gets:
- Substituting this into the equation for current density:
- The electric field is independent of v, so can be pulled out of the integral:
- Finally:
- The integration over the longitudinal part is difficult. But at high frequencies:
- The the integrand can be approximated:
- At T=105K and 100kHz:
- So for this subject no kinetic treatment is necessary !

---
Theory: Other dielectric tensors
- There is a complicated dielectric tensor for magnetized kinetic plasmas. This tensor is not relevant due to the result of the last slide.
- At high temperatures the kinetic model would be necessary. Then also the relativistic effects and the radiation would have to be taken into account.
- Quantum mechanical model necessary ? The criterion is
- For electrons:
- Which is always true in the scope of this subject.

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Modeling the plasma sheath
- Conclusion + Outlook

---
Antenna Theory: Green's function
- In this context Green's function is a dyadic function.
- It maps an infinitesimal source to the responding field.
- The wave equation for the electric field :
- It can be solved when the Green's function is found:
- This equation is independent of the medium. The whole plasma physics is insider Green's function.
- Combining the two equations gives:
- Fourier transforming and manipulating gives:
- And finally
- To use, a FT to real space has to be performed.

---
Antenna theory: Cold isotropic Green's function
- For the isotropic cold plasma the solution turns out to be:
- Where g is the Green's function in vacuum:
- So the electric field equation is:
- And the electric field integral equation, EFIE would be
- This equation is the boundary condition of an electric field on a conducting surface. It says, that the tangential field of the incident field is equal to the tangential component of the scattered field.
- This equation is used in NEC to compute the mutual impedances between the segments to create the matrix.
- Certain assumptions are made for facilitation: thin wires, where only axial currents are used.

---
Antenna theory: cold magnetized plasma
- Using a special form of the radiation tensor:
- Green's function can be written as
- To my knowledge the integral can not be solved analytically.
- It would have to be solved together with:
- Numerically as the inner integral in a system of 2 nested integrals.

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Modeling the plasma sheath
- Conclusion + Outlook

---
Dipole Radiation
- A 1D MoM solver was written and calculations where performed with a 6m dipole.
- The MoM code uses pulse functions.
- A second solver, using sinusoidal functions, was written and produces the same results.
- The feed is across a segment.
- The isotropic cold plasma model was implemented.

---
Dipole Radiation
- After many test-calculations in vacuum, field calculations where performed, using currents computed with vacuum conditions.
- In this simple model, the main difference is an elongation of wavelength.
- This corresponds to a smaller effective length vector.
- A lower field intensity is expected because energy is stored in the oscillation of the plasma particles: ordered kinetic energy.

---
Dipole Radiation
Including the effect of the ions is of magnitude due to the mass relation of the particles.

---
Dipole Radiation
- Investigating the currents and Impedances, it can be seen that the net effect is a reduction of the lengths of the effective length vectors.
- This is the unrealistic situation where the relation of plasma frequency to frequency is constant over the whole frequency range.

---
Dipole Radiation
- Here a realistic case.
- ωpe = 10MHz
- This result suggests that a vacuum approximation is valid for many situations.

---
Dipole Radiation
But near resonances the situation can be different.

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Modeling the plasma sheath
- Conclusion + Outlook

---
STEREO Antennas
- Calculations of the S-WAVES antennas where performed.
- The Stereo mission comprises 2 spacecraft.
- Both are nearly at earth orbit around the sun, one ahead of earth, one behind.
- They drift apart to get a stereographic view with different angles.
- Solar radiation is received with the antennas.

---
STEREO Antennas
- The calculations where performed with Concept II.
- In Concept the real and imaginary part of the permittivity can be altered.
- By setting the real part, a simple cold isotropic plasma can be simulated.

---
STEREO Antennas: Impedances

---
STEREO Antennas: Effective length vectors

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Modeling the plasma sheath
- Conclusion + Outlook

---
Plasma sheath
- Conductive surfaces interact with surrounding plasma.
- Around the immersed object a plasma sheath forms.
- This sheath can vary, depending on the charge of the object (positive or negative).
- The sheath can be modeled as capacity which is easily included in the antenna calculation.
[Bale et. al. 2007]

---
Plasma sheath
- 2 or three currents flow between S/C and plasma.
- In equilibrium the sum of the currents is zero.
- Depending on the photoelectron current the S/C is charged positively or negatively.
- Different physical effects.
-
-
+
Ion current
Electron
current
Photoelectron
current

---
Plasma sheath, negative charge
- No solar radiation → S/C negatively charged.
- If electrons and ions are in thermal equilibrium, mean electron speed is higher.
- → more electrons hit the surface.
- → negative charge builds up.
- → thermal electrons are pushed away by charge.
- → Ions are attracted.
- → electrons depletion sheath forms.
- → the thickness of the sheath regulates itself in a way that the sum of the currents are equal.

---
Plasma sheath, negative charge
- Thermal electrons are postulated to be Maxwell distributed.
- Conservation of energy:
- Particle density: zeroth moment.
Current: first moment x charge

---
Plasma sheath, negative charge
- All ions reach the surface.
- They fall into a potential well.
- → acceleration
- → density decreases due to mass conservation.
- Energy conservation.
- Combining the conservation laws yields equation for particle density.
- From this the ion current can be derived.

---
Plasma sheath, negative charge
- Photoelectrons are created by the photoelectric effect.
- Usually solar radiation.
- All photoelectrons reach the plasma.
- iph depends on energy distribution of the photons and on geometry and material of the S/C.
- AΦ...illuminated cross section.
- Speed and density as for ions..

---
Plasma sheath, negative charge
- Boundary conditions:
- The currents are summed to zero.
- Quasi neutrality postulated.
- Influence of ions small.
- Sheath thickness can be estimated as the Debye length or one calculates the potential and density distribution across the sheath.

---
Plasma sheath, negative charge
- To calculate the potential distribution, Poisson's equation has to be solved:
- This equation is non-linear and can not be solved analytically. But it can be linearized if
- Then a Taylor approximation can be used:
- Neglecting the photoelectrons and assuming quasi-neutrality, the result is
- The solution:

---
Plasma sheath, negative charge
- Sheath resistance is the gradient of the V-I curve.
- Explicit expression by [Gurnett 2000]
- At high frequencies the resistance can be neglected.
For the capacity I use the formula of a cylindrical capacitor.

---
Plasma sheath, positive charge
- Photo-electrons dominate.
- Again, the currents sum up to zero.
- →S/C is charged positively. Number of photoelectrons reaching the plasma (only a few %) == number of thermal electron reaching the surface.
- Most photoelectrons have too low energy and fall back to the surface from which they are attracted.
- They form an electron-sheath.
- They are not part of the photo-electron current.

---
Plasma sheath, positive charge
- All thermal electrons reach the surface → no Boltzmann
- Only photoelectrons which are energetic enough reach the plasma.
- Photo-electrons nearly Maxwell-distributed [Grard et. al].
- Photo-electron backflow:
- Photo-electron current == thermal electron-current.
- → total backflow:
- Potential:

---
Plasma sheath, positive charge
- Poisson equation, 1D over flat surface:
- Or
- Linearizion:
- With assumed quasi-neutrality:
- Which gives:

---
Plasma sheath, positive charge
- In cylindrical coordinates:
- Linearized:
- Can be brought into the form of a Sturm Luiville problem:
- With the solution:
- and

---
Plasma sheath, positive charge
- The sheath resistivity:
- Using just the photoelectrons, one can write:
- Then
- As before
- But now using the mean permittivity:

---
Plasma sheath, STEREO
- Using the equations presented before:
- the S/C is positively charged and 5.5V is in accordance with experience of similar missions.
- The Debye length of the photoelectrons:
- Using the derived formula:
- This gives:
- Bale gives a capacity of 40pF

---
Plasma sheath, STEREO

---
Content
- Introduction
- The method of moments (MoM)
- Theory (Plasma-Electrodynamics)
- Theory (Antenna Theory)
- Analysis of a dipole radiation
- Application on STEREO antennas
- Modeling the plasma sheath
- Conclusion + Outlook

---
Outlook
- Only the most simple situation has been treated, cold isotropic plasma.
- It has been shown that kinetic treatment is not necessary.
- Including the effect of magnetized plasma would be interesting, because S/C typically operate in such an environment.
- Using the FDTD method, it would be easier to implement anisotropy.
- Also isotropic results could be verified.
- But there is probably another way to implement anisotropic plasma in MoM simulations without having to use the dielectric tensor.
- In this simple dielectric plasma model, plasma manifests itself as a change in wavelength and therefore phase speed.
- By scaling the model, the same results can be achieved.

---
Outlook
Calculation	Impedance
Dipole, 6m, ε=1, r=2mm	6.882736497964838e-03 - 7.112228243779676e+04i
Dipole, 6m, ε=0.5, r=2mm	3.441273366066885e-03 - 1.005881770038659e+05i
Dipole, 6m *sqrt(ε), ε=1, r=2mm*sqrt(ε)	3.441273374398452e-03 - 1.005881770038794e+05i

---
Outlook

---
Outlook
- Unfortunately this does not work with all solvers. But it is easier to write a solver which adheres to the invariance of Maxwell's equations at scaling, than to write one which can cope with dielectric tensors.
- Magnetized plasma could be modeled by scaling the model an-isotropically
- It remains to analyze how the imaginary tensor elements are to be dealt with.
- The plasma sheath theory should be refined and synchronized with existing results and ongoing research.
- It is possible to simulate the sheath realistically by using particle simulations or particle-in-cell simulations.

---
Thank you for your attention !